INSERTION AND MAINTENANCE OF BD SAF-T-INTIMA™

The Saf-t-intima™ is a closed IV catheter system. It is recommended for use in continuous subcutaneous (S/C) infusions and for the administration of breakthrough doses of medicine.

Ensure all medication given S/C is recommended for S/C use. It is best to use one site for continuous infusion and another if possible for breakthrough doses.

Having a second Saf-t-intima™ insitu will ensure incompatible drugs are not mixed.

Physical assessment of the patient is required to select an insertion site.

- Avoid skin folds or line of clothes. The abdomen, thigh and upper arm are all appropriate sites, as depicted within the squares below. The abdomen is considered site of choice.

- Ongoing assessment includes daily observation of the Saf-t-intima™, insertion site for redness, swelling, exudate, bleeding or difficulty injecting.

EQUIPMENT

- 1x Saf-t-intima™ catheter with tegaderm

- 1x alcohol wipe

- Local anaesthetic cream and tegaderm, or ice (if required, based on patient preference. Local anaesthetic cream is the most effective)

- Oral sucrose 33% should be used for procedural pain relief in infants aged less than 3 months of age. Refer to oral sucrose for procedural pain management in infant’s guideline.

NB: All orders for oral sucrose 33% and/or local anaesthetic cream must be documented on the patient’s medication chart (MR 690/A) as per RCH medication policy.

CAUTION: REMOVE THE WHITE CLAMP AND PLACE ABOVE THE Y- PORT.

PROCEDURE

- Wash hands and assemble equipment.

- Utilise personal protective equipment including non sterile gloves.

- Select an insertion site.

- If required, based on patient age and preference:

  - Apply local anaesthetic cream to the site 30-60 minutes prior to insertion.
or

  - Apply ice to the insertion site until numb.
or

  - Administer oral sucrose 33%.

- After appropriate length of time has elapsed, apply alcohol gel to hands, allow to dry prior to donning non sterile gloves.

- Clean the selected site with an alcohol swab and allow to dry.

- Open the package containing the Saf-t-intima™ and dressing by pulling the paper lid from the plastic package.

- Remove needle cover and inspect unit

- Secure flow control plug or remove it to pre-prime/pre-connect system, if required

NB: As the dead space volume of the Saf-t-intima™ catheter is 0.0075 ml, it is unnecessary to flush the Saf-t-intima™ before or after use unless more than 10% of the dose will be lost in the dead space. In this situation consult the Medical Officer and Pharmacy as a small amount of compatible solution may be considered to flush the medication.

CAUTION: REMOVE THE WHITE CLAMP AND PLACE ABOVE THE Y- PORT.

- Holding catheter as illustrated, rotate safety barrel to loosen needle

- Make sure bevel is oriented and not covered by the catheter; hold the pebbled sides of flange to ensure they are in contact with the skin surface when the catheter is placed.

- Advance the Saf-t-intima™ into the subcutaneous space the total length of the catheter at a 20 to 45 angle to the skin surface i.e. towards the shoulder joint in the arm, towards the hip in the leg, horizontal and towards the umbilicus in the abdomen.

- This should be done in one quick, smooth movement with the bevel facing up.

- Release wings and stabilise with tegaderm dressing

- Grasp white shield and pull back slightly to recess needle

- Shield will come off, exposing the adapter

- Place needles in a puncture-resistant, leak-proof sharps container.

NB: Do not reinsert the needle if catheter is dislodged/withdrawn.  Repeat the procedure with a new Saf-t-intima™.

- Dispose of the needle in a sharps container.ensure the insertion site is visible through the plastic window and the hub is open to air.

- Totally adhere dressing to skin to prevent bacteria from entering insertion site.

- Change the rubber bung on the Y port to a red cap OR smart syte bung.

- Write date of insertion on the dressing.

- Complete appropriate documentation.

CAUTION REMINDERS

- Do Not bend the needle prior to insertion.

- Never Reinsert Needle into the catheter as this could shear the catheter.

- Do Not Use Scissors at or near the insertion site.

- Place all needles in a puncture-resistant, leak-proof sharps container.

CAUTION: REMOVE THE WHITE CLAMP AND PLACE ABOVE THE Y- PORT.

SITE MAINTENANCE

- The Saf-t-intima™ should be rotated to a different site after a maximum of 7 days or sooner if there are any complications.

- The Saf-t-intima™ should be inserted in the same direction as venous return- i.e. towards the shoulder joint in the arm, towards the hip in the leg, horizontal and towards the umbilicus on the abdomen.

- Remove the Saf-t-intima™ when the prescribed injections have ceased.

Complications related to the insertion of an Saf-t-intima™ include:

- Infection

- Discomfort

- Blockage

Signs and symptoms:

- Redness

- Inflammation

- Exudate

- Bruising

- Pain

- Leakage

MANAGEMENT

The Saf-t-intima™ should be removed and a new one placed at a different site. Any of the above signs and symptoms should be documented in the patient's medical record

DOCUMENTATION

• The following should be documented in the patient medical records:

• All medications administered to be recorded on the medication chart (MR690/A)

• The date, procedure and site of insertion.

• Daily observation of insertion site for signs of complications.

• The date and reason for removal of the Saf-t-intima™.

PREPARATION

• Prepare site according to policy and procedure

• Remove needle cover and inspect unit

• Secure flow control plug or remove it to pre-prime/pre-connect system

• Holding catheter as illustrated, rotate safety barrel to loosen needle

• Make sure bevel is oriented and not covered by the catheter

INSERTION

• Grasp pebbled side of wings, pinching firmly

• Approach skin slowly at a low angle

• Observe flashback in tubing behind wings

ADVANCEMENT

• Lower catheter almost parallel to the skin

• Advance the ENTIRE UNIT to ensure catheter tip is placed subcutaneously

• Release wings and stabilize with tegaderm dressing

• Grasp white shield and pull back slightly to recess needle

NEEDLE REMOVAL

• Stabilize catheter wings

• Grasp white shield and pull in a straight continuous motion

• Shield will come off, exposing the adapter

• Place needles in a puncture-resistant, leak-proof sharps container.

SECUREMENT

• Secure catheter and apply sterile dressing according to policy

and procedure

CAUTION REMINDERS

• Do Not bend the needle prior to insertion.

• Never Reinsert Needle into the catheter as this could shear the catheter.

• Do Not Use Scissors at or near the insertion site.

Place all needles in a puncture-resistant, leak-proof sharps container.

TIPS FOR SUCCESS

MAINTAINING THE BEVEL POSITION

• Make sure the pebble side of catheter wings is in contact with the fingers

• Pinch the wings tightly near the base to ‘lock’ the bevel position

MAKING A SMOOTH INSERTION

• Make sure catheter is not over needle bevel

• Maintain traction on the skin

INSERTION SUCCESS

• Slow down the speed of insertion

• Lower the initial insertion angle keeping the elbow low

• After flash, lower the angle and advance

• Make sure tip seal is released by rotating the safety barrel

THREADING WITH EASE

• Make sure to release the tip seal before insertion by rotating the safety barrel

• After insertion of the needle, lower the angle and advance

• Do not pull back on the white shield initially more than 1/8 inch

• Maintain traction on the skin

REMOVING THE NEEDLE EASILY

• Make sure to release the tip seal before insertion by rotating the safety barrel

• Open the catheter wings flat

• Do not place finger(s) on the center of the wings

• Only grasp the pebbled end of the white shield

• Without hesitating, pull the needle out in a straight continuous motion until the shield pops off

ACTIVATING THE SAFETY SHIELD

• Only grasp the pebbled end of the white shield

• Without hesitating, pull the needle out in a straight continuous motion until the shield pops off

CAUTION: REMOVE THE WHITE CLAMP AND PLACE ABOVE THE Y- PORT.